## Slide 1
TOPIC:
Direct Memory Access (DMA)
By-
Dr. Bineet Kaur (Asst. Prof., DICE)

## Slide 2
Direct Memory Access

## Slide 3
In DMA, the CPU is idle and the peripheral device manage the memory buses directly.
● DMA controller takes over the buses to manage the transfer directly between the I/O device and memory.
● The DMA transfer can be made in several ways.
● Burst Transfer - A block of memory words is transferred in a continuous burst at a time. Used for fast devices such as magnetic disks, where data transmission cannot be stopped or slowed down until an entire block is
transferred.
● Cycle Stealing - Allows the DMA controller to transfer one data word at a time, after which it must return control of the buses to the CPU.
The CPU merely delays its operation for one memory cycle to allow the
direct memory I/O transfer to “steal” one memory cycle.
Direct Memory Access

## Slide 4
Working of DMA
The Bus Request (BR) input is used by the DMA controller to request the CPU to relinquish control of the buses.
● When this input is active, the CPU terminates the execution of the current instruction and places the address bus, the data bus, and the read and write lines into a high-impedance state.(like an open circuit)
● The CPU activates the Bus Grant (BG) output to inform the external DMA that the buses are in the high-impedance state.(available)
● The DMA takes control of the buses to conduct memory transfers without processor intervention.
● When the DMA terminates the transfer, it disables the bus request line and the CPU disables the bus grant, takes control of the buses, and returns to its normal operation.

## Slide 5
Direct and Indirect Addressing Modes
The registers in the DMA are selected by the CPU through the address bus by enabling the DMA Select (DS) and Register Select (RS) inputs.
● When the BG (bus grant) = 0, the CPU can
communicate with the DMA registers.
● When BG = 1 DMA can communicate directly with the memory.
● The DMA controller has three registers.
● The Address register contains an address to specify the desired location in memory.
● The Word Count Register holds the number of words to be transferred.
● The Control Register specifies the mode of transfer.
● The DMA communicates with the external peripheral through the request and acknowledge lines.

## Slide 6
I/O Device sends a DMA request.
➜ DMA Controller activates the BR line.
➜ CPU responds with BG line.
➜ The DMA puts the current value of its address register into the address bus, initiates the RD or WR signal, and sends a DMA acknowledge to the I/O device.
➜ I/O device puts a word in the data bus (for
write) or receives a word from the data bus
(for read).
➜ The peripheral unit can then communicate
with memory through the data bus for direct
transfer between the two units while the CPU
is momentarily disabled.
DMA Transfer

## Slide 7
➜ For each word that is transferred, the DMA
increments its address register and decrements its word count register.
➜ If the word count does not reach zero, the DMA checks the request line coming from the I/O Device.
➜ If there is no request ,the DMA disables BR so that the CPU continues to execute its own program.
➜ When CPU requests another transfer, DMA
requests bus again.
➜ If the word count register reaches zero, the DMA stops any further transfer and removes its bus request. It also informs the CPU of the termination by an interrupt.
DMA Transfer

## Slide 8
  Thank You