## Slide 1
TOPIC:
Program Control, Program Control: Status bits, Conditional Branch Instructions, Subroutines call and return Program Interrupts & Types
Dr. Gaurav Sharma
Associate Professor
DICE-CUIET

## Slide 2
Data Transfer and Manipulation
Instruction set of different computers differ from each other mostly in
way the operands are determined from the address and mode fields.
The basic set of operations available in a typical computer are :
  Data Transfer Instructions
  Data Manipulation Instruction :
perform arithmetic, logic and shift operation
  Program Control Instructions
decision making capabilities, change the path taken by the
program when executed in computer.

## Slide 3
Data Transfer Instructions
Load LD
Store ST
Move MOV
Exchange XCH
Input IN
Output OUT
Push PUSH
Pop POP
Name Mnemonic
Typical Data Transfer Instructions
Move data from one place in computer to another without changing
the data content
Most common transfer : processor reg -memory, processor reg -I/O,
between processor register themselves

## Slide 4
Data Transfer Instructions
Direct address LD ADR AC M[ADR]
Indirect address LD @ADR AC  M[M[ADR]]
Relative address LD $ADR AC  M[PC + ADR]
Immediate operand LD #NBR AC  NBR
Index addressing LD ADR(X) AC  M[ADR + XR]
Register LD R1 AC  R1
Register indirect LD (R1) AC  M[R1]
Autoincrement LD (R1)+ AC  M[R1], R1  R1 + 1
Autodecrement LD -(R1) R1  R1 - 1, AC  M[R1]
Mode
Assembly
Convention
Register Transfer
Data Transfer Instructions with Different Addressing Modes
Some assembly language conventions modify the mnemonic symbol to differentiate
between the different addressing modes

## Slide 5
Data Manipulation Instructions
Three Basic Types:
Arithmetic instructions
Logical and bit manipulation instructions
Shift instructions
These instruction performs operation on data and provide the computational
capabilities for the computer

## Slide 6
Data Manipulation Instructions
Arithmetic Instructions
Name Mnemonic
Increment INC
Decrement DEC
Add ADD
Subtract SUB
Multiply MUL
Divide DIV
Add with Carry ADDC
Subtract with Borrow SUBB
Negate(2’s Complement) NEG
Four basic arithmetic operations : + - * /

## Slide 7
Data Manipulation Instructions
Clear CLR
Complement COM
AND AND
OR OR
Exclusive-OR XOR
Clear carry CLRC
Set carry SETC
Complement carry COMC
Enable interrupt EI
Disable interrupt DI
Name Mnemonic
Logical and Bit Manipulation Instructions
Logical Instructions perform binary operations on string of bits stored in registers
Useful for manipulating individual/ group of bits
 Consider each bit separately
AND Clear selected bits
OR Set selected bits
XOR Complement selected bits

## Slide 8
Data Manipulation Instructions
Logical shift right SHR
Logical shift left SHL
Arithmetic shift right SHRA
Arithmetic shift left SHLA
Rotate right ROR
Rotate left ROL
Rotate right thru carry RORC
Rotate left thru carry ROLC
Name Mnemonic
Shift Instructions

## Slide 9
Program Control Instruction
PC
+1
In-Line Sequencing (Next instruction is fetched from the next adjacent location in the memory)
Address from other source; Current Instruction, Stack, etc; Branch, Conditional Branch, Subroutine, etc
Program Control Instructions
Name Mnemonic
Branch BR
Jump JMP
Skip SKP
Call CALL
Return RTN
Compare(by  ) CMP
Test(by AND) TST
* CMP and TST instructions do not retain their
results of operations (  and AND, resp.).
They only set or clear certain Flags.
like carry /sign/zero bit or overflow condition

## Slide 10
Flag, Processor Status Word
In Basic Computer, the processor had several (status) flags – 1 bit value that indicated various information about the processor’s state – FGI, FGO, I, IEN, R
In some processors, flags like these are often combined into a register – the processor status register (PSR); sometimes called a processor status word (PSW)
Common flags in PSW are
  C (Carry): Set to 1 if the carry out of the ALU is 1
  S (Sign): The MSB bit of the ALU’s output
  Z (Zero): Set to 1 if the ALU’s output is all 0’s
  V (Overflow): Set to 1 if there is an overflow
Status Flag Circuit
c7
c8
A B
8 8
8-bit ALU
V Z S C
F7
F7 - F0
8
F
Check for
zero output

## Slide 11
Status Bit Condition
Status Bit | Description | Set to 1 | Clear to 0
C | Carry | If end carry C8 =1 | If carry=0
S | Sign | Highest order bit F7=1 | If F7=0
Z | Zero | O/P of ALU contains all 0 | otherwise
V | Overflow | EX-OR of last two carries=1 | otherwise

## Slide 12
Conditional Branch Instruction
BZ Branch if zero Z = 1
BNZ Branch if not zero Z = 0
BC Branch if carry C = 1
BNC Branch if no carry C = 0
BP Branch if plus S = 0
BM Branch if minus S = 1
BV Branch if overflow V = 1
BNV Branch if no overflow V = 0
BHI Branch if higher A > B
BHE Branch if higher or equal A  B
BLO Branch if lower A < B
BLOE Branch if lower or equal A  B
BE Branch if equal A = B
BNE Branch if not equal A  B
BGT Branch if greater than A > B
BGE Branch if greater or equal A  B
BLT Branch if less than A < B
BLE Branch if less or equal A  B
BE Branch if equal A = B
BNE Branch if not equal A  B
Unsigned compare conditions (A - B)
Signed compare conditions (A - B)
Mnemonic Branch condition Tested condition
Notes: Unsigned A= 11110000 B= 00010100 C=1, S=1, V=0, Z=0

## Slide 13
Subroutine Call and Return
Call subroutine
Jump to subroutine
Branch to subroutine
Branch and save return address
First Location in the subroutine (Memory)
Fixed Location in memory
In a processor Register
In memory stack
- most efficient way
Subroutine Call
Instructions are executed by performing two operations :
(1). Save PC as Return Address to get the address of the location in the Calling Program
upon exit from the Subroutine
(2). Branch to the beginning of the Subroutine
- Same as the Branch or Conditional Branch
Locations for storing Return Address
CALL
SP  SP - 1
M[SP]  PC
PC  EA
RTN
PC  M[SP]
SP  SP + 1
Subroutine : self contained sequence of instructions that performs a given computation task

## Slide 14
Interrupt Procedure
Program Interrupt refers to the transfer of program control from
a currently running program to another service program as a
result of an external or internal generated request

## Slide 15
Interrupt Procedure
- The interrupt is usually initiated by an internal or an external signal rather than from the execution of an instruction (except for the software interrupt)
- The address of the interrupt service program is determined by the hardware rather than from the address field of an instruction
- An interrupt procedure usually stores all the information necessary to define the state of CPU rather than storing only the PC.
The state of the CPU is determined from:
      Content of the PC
      Content of all processor registers
      Content of status bits
Many ways of saving the CPU state
depending on the CPU architectures
Interrupt Procedure and Subroutine Call

## Slide 16
Interrupt Procedure
- CPU does not respond to interrupt until end of instruction cycle,
checks just before next fetch phase
- If interrupt pending, control passed to h/w interrupt cycle:
- Content of PC and PSW is pushed into stack
- branch address of interrupt transferred to PC and new PSW
loaded into status registers
Service Program executed starting from branch address and
status of CPU as specified by new PSW
Last instruction from service program is return from interrupt
instruction

## Slide 17
Program Interrupt
Types of Interrupts
External interrupts
External Interrupts initiated from the outside of CPU and Memory
- I/O Device → Data transfer request or Data transfer complete
- Timing Device → Timeout
- Power supply  Power Failure
Internal interrupts (traps)
Internal Interrupts are arises from illegal or erroneous use of instn. or data
- initiated by program itself rather than external event
- Register, Stack Overflow
- Divide by zero
- OP-code Violation
- Protection Violation
Software Interrupts
Both External and Internal Interrupts are initiated by the computer HW.
Software Interrupts are initiated by the executing an instruction.
- Supervisor Call 1. Switching from a user mode to the supervisor mode
2. Allows to execute a certain class of operations
which are not allowed in the user mode